## Slide 1: Thesis Proposal Idea
Genetic algorithm to train a batbot to hover
Anuar santoyo alum
2023/02/20

## Slide 2: TABLE OF CONTENT
Problem Statement
General Optimization Workflow
Static Hovering Test
Dynamic Hovering Test
* MORE DETAILED INFORMATION

## Slide 3: Problem Statement
Goal: Batbot to achieve stable hovering.
Problem: Complex control strategy as flapping wings are much more complex compared to for example a quadcopter.
Solution: Design a testing environment were, by means of a genetic algorithm, the Batbot can safely learn by itself the necessary controls to achieve hovering.

## Slide 4: PROBLEM Statement - How can this be achieved?
Static Hovering Test
Batbot fixed to a point to learn basic movement needed to hover.
Dynamic Hovering Test
Batbot allowed to fly without attachments to train control system based on results of static hovering test.
Problem: Training might need a lot of repetitions which is difficult when training in real world and not in simulation.
Solution: 2 Step Training( 1st Static, 2nd Dynamic)

## Slide 5: General optimization WORKFLOW
1st Step: Evolutionary algorithm Covariance Matrix Adaptation (CMA) proposes n solutions (solution varies from test to test)
2nd Step: n Tests are carried out in the test bench and using the sensors a score is calculated for each test
3rd Step: Scores of the tests are given back to the computer so that the CMA can use information to propose other n solutions
n Solutions
Computer running CMA
n Tests in Testbench
n Scores
* WHY CMA?

## Slide 6: Static hovering test
Solution:
ONLY Motor Commands
MultiAxial Force Torque Sensor
Micro-controller that enables wireless communication:
Scores of Tests
* SENSOR POSITION ON ROBOT NEEDS DYNAMICS ANALYSIS AND CENTER OF MASS
*HOW IS SCORE CALCULATED
-ESP8266
-Arduino UNO WiFi Rev.2
-Raspberry Pi Zero 2 W
-….
IMPORTANT: Result of this test only gives direct command to motors (no controlling yet) to obtain approximate power needed in each motor to hover in perfect conditions.
NOT ABLE TO AUTONOMOUSLY FLY YET

## Slide 7: dYNAMIC hovering test (free flight enabled)
Force Sensor
String
Position Sensor
*Extreme simplification, several ideas for position sensor: Array of US sensor, Camera and OpenCV Python,, OptiTrack alternative
Solution:
Controling System that uses BatBot accelerometer as input and controls Batbots motors (not just direct motor command, like in static test)
Scores
Solutions

## Slide 8
ControlLing system optimization
Accelerometer
Neural Network
Batbot Motors
*Traditional controlling methods can also be optimized using evolutionary algorithm

## Slide 9
Summary
Static Hovering Test: Optimizes direct motor command to approximate hovering
Dynamic Hovering Test: Uses results of Static Hovering Test as starting point to optimize controlling system to hover.

## Slide 10: Thank you!