## Slide 1: Batbot Control Parameters Optimization Through Evolutionary Algorithm
MASTER THESIS ORAL DEFENSE
Anuar Santoyo alum 安武 2022280136
Supervisor: Prof. ZHANG YUN张云
2024/05/28

## Slide 2: TABLE OF CONTENT
Batbot
Evolutionary Algorithm
Experiments and Design Optimization
Bio-mimick Optimization

## Slide 3: BATbot - Design
Page 1
  Inspired in the fruit bat
  6 DOF:
    Flapping
    2 DOF per hind leg (4 DOF)
    Extension of wing
  Carbon fiber body
  Silicone elastic membrane
  Magnetic Encoder for wing angle

## Slide 4
Batbot - controlling
How to find the best strategy of hind-leg movement for highest force?
Page 2

## Slide 5
Batbot - controlling
How to find the best strategy of hind-leg movement for highest force?
Try all possible combinations:
  1 dim: 10 * 6s = 1min
  5 dim: 10^5*6s = 167 hours = 1 week
Simulation
  Elastic Membrane and Fluid Dynamic
Solution: EA Strategy
(X, Y) mid. point
Page 2

## Slide 6: Evolutionary algorithm - General
1st Step: Evolutionary algorithm Covariance Matrix Adaptation (CMA) proposes 10 solutions (Ex. Angle and amplitude)
2nd Step: 10 Tests are carried out in the test bench and using the sensors a score is calculated for each test
3rd Step: Scores of the tests are given back to the computer so that the CMA can use information to propose other 10 solutions
10 Solutions
Computer running CMA
10 Tests in Testbench
10 Scores
Page 3

## Slide 7
Evolutionary algorithm - workflow
Computer - Python
Wireless UART
Batbot with PyBoard (MicroPython)
Measurements
6 Axis Measurements
Page 4

## Slide 8
Evolutionary algorithm - testbench
Testbench and Measurements
Fz
Fy
Page 5

## Slide 9
Experiments and design optimization – Frequency vs force
Experiment with increasing power to analyze average lift and resulting average force for a 7N heavy Batbot
Page 6

## Slide 10
Experiments and design optimization – Frequency vs force
Initial experiment WITHOUT controlling
Why are 3N enough to make Batbot fly?
→ wing foil does not generate lift in hovering.
Need to upgrade Batbot to achieve higher forces for hovering.
Page 7

## Slide 11
Experiments and design optimization - Batbot upgrade
UPGRADE
2 main gears
50 Amp Electronic Speed Controller
100 W DC Motor
Higher Flapping Amplitude
Page 8

## Slide 12
Experiments and design optimization -
Dynamic Test-bench test
Safe multiple hovering tests
Realistic circumstances
If hovering, Batbot drawn to center, otherwise a force is measured.
With Hookes Law position known from force
  F = k*x
Force
Position
Page 9

## Slide 13: Experiments and design optimization Dynamic test-bench results
Experiments Result: Upgraded version of Batbot is capable of generating enough lift to hover.
Page 10

## Slide 14
Experiments and design optimization - Outdoors experiments Tied
Experiment Result: Batbot lifts and is relatively stable..
Page 11

## Slide 15
Experiments and design optimization - Outdoors experiments Rotation
Experiment Result: It is possible to control to a certain degree the rotation of the Batbot mid-flight
Page 12

## Slide 16
Experiments and design optimization
Outdoors experiments free flight
Experiment Result: Initial free hand controlled hovering experiments as a starting point to be refined using the optimization algorithm.
Page 13

## Slide 17: Experiments and design optimization - PID
Developed working feedback control using PID and MPU Sensor
Page 14

## Slide 18: Experiments and design optimization - pid
Flight Test Using PID was successful
Batbot mechanical and electronical design phase concluded
Next step:
  Use of EA to obtain controlling strategy
Page 15

## Slide 19
Biomimicking – real bat data
Thanks to Dr. Singh’s dissertation “Kinematic Analysis of a Bat Flight Based on Membrane Wing Motion Reconstruction” we obtained valuable data on the real bat flight data.
Page 16

## Slide 20
Biomimicking - optimization
Find optimal:
X amplitude (horizontal)
Y amplitude (vertical)
Y neutral angle
Phase shift between wing and tail flapping
Page 17

## Slide 21
Biomimicking - result
Results:
Constant improvement
Within 25 generations convergence is achieved
25 Generations
* 10 Test = 250 Tests
250 Tests * 6s = 25 min
in only 25 min!
Instead of 1 week
Page 18

## Slide 22
Biomimicking - result
Results:
Clear convergence to an optimal solution
Solution identical to real bat data
REAL BAT DATA
EA and the Batbots design are functional and accurate.
Page 19

## Slide 23
conclusion
Developed EA for complex robot controlling
Used EA to optimize Batbot and its design to achieve controlled flight
Validated design and system with real bat data (future step, publish results)
Page 20

## Slide 24
Academic achievements
As part of the double degree program between the Technical University of Berlin and Tsinghua University I:
Published:
  Santoyo Alum, A.; Fay, T.-A.; Cigarini, F.; Göhlich, D. Assessment of Thermal Comfort in an Electric Bus Based on Machine Learning Classification. Appl. Sci. 2023, 13, 11190.
  Parameter Optimization of Additive Manufacturing Process LPBF Using an Evolution Strategy Algorithm Applied on the Material Tungsten Carbide Cobalt WC – Co 83/17 Eckart Uhlmann, Julian Polte, Josué Dávila Cherres, Jaroslaw Kochan and Anuar Santoyo Alum. Advance in material Science, vol 64. chapter 8
  Jing-Shan Zhao, Han-Lin Sun, Xiao-Cheng Sun, Anuar Santoyo Alum. Tension Optimization of Cable-driven Robot by Screw Statics, 6th IEEE/IFToMM International conference on Reconfigurable Mechanism Robots
Conference
  “Assessment of Thermal Comfort in an Electric Bus Based on Machine Learning” Anuar Santoyo Alum, Classification 2nd International Virtual Conference on Materials Science and Engineering held during November 11-12, 2023
Page 21

## Slide 25
Academic achievements
As part of the double degree program between the Technical University of Berlin and Tsinghua University I:
Submitted:
  Hybrid design and biomechanics tests of a robotic bat with morphing membrane wings. Jinghu Li, Anuar Santoyo Alum, Jing-Shan Zhao, 24th IFToMM China International Conference on Mechanism and Machine Science & Engineering
Working on:
  EA to validate Batbot controlling strategy with real bat data., Kunar Singh Sudeep, Anuar Santoyo Alum
Awards
  International Student Scholarship Tsinghua University, Department of Mechanical Engineering 2023
Page 22

## Slide 26: Thank you for your attention!
More than happy to answer any question

## Slide 27
appendix

## Slide 28
appendix

## Slide 29
appendix

## Slide 30
appendix

## Slide 31
appendix

## Slide 32
appendix

## Slide 33
appendix